## Slide 1: Vehicle Dynamics Library
Sri Venkata Satya Prasad Maddipatla
Intelligent Vehicles and Systems Group
Department of Mechanical Engineering

## Slide 2: It is believed that vehicle behavior can be better predicted by modeling the vehicle like a bicycle or dual track.
Bicycle
Dual Track

## Slide 3: Bicycle model
CG
a
b

## Slide 4: Slip angles at each tire of a vehicle represented by the bicycle (single-track) model are given by
function slip_angles = fcn_VD_stSlipAngle(U, V, r, steering_angle, vehicle)
%% fcn_VD_stSlipAngle
% This function computes slip-angles for front and rear wheels. It
% uses a single-track/bicycle model.
%
%% Calculate Slip-Angles
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
wheel_velocity = fcn_VD_stWheelVelocity(U,V,r,vehicle); % calculate wheel velocities
slip_angles = atan(wheel_velocity(:,2)./wheel_velocity(:,1))-steering_angle; % Slip angle
end

## Slide 5: `fcn_VD_stSlipAngle’ estimates slip angle
%% script_test_fcn_VD_stSlipAngle.m
% This script tests MATLAB function 'fcn_VD_stSlipAngle'
%
% Author: Satya Prasad on 2021/08/13
% Questions or comments? szm888@psu.edu
%% Prepare the workspace
close all; % close all the plots
clear all %#ok<CLALL>
clc
%% Add path
addpath('../VD_Utilities')
addpath('../VD_Utilities/Bicycle')
%% Inputs
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% _____ _
% |_ _| | |
% | | _ __ _ __ _ _| |_ ___
% | | | '_ \| '_ \| | | | __/ __|
% _| |_| | | | |_) | |_| | |_\__ \
% |_____|_| |_| .__/ \__,_|\__|___/
% | |
% |_|
% See: http://patorjk.com/software/taag/#p=display&f=Big&t=Inputs
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%% Define vehicle properties
% Define a MATLAB structure that specifies the physical values for a vehicle.
% For convenience, we ask that you call this stucture 'vehicle'.
vehicle.m = 1600; % mass (kg)
vehicle.Izz = 2500; % mass moment of inertia (kg m^2)
vehicle.Iw = 1.2; % mass moment of inertia of a wheel (kg m^2)
vehicle.Re = 0.32; % effective radius of a wheel (m)
vehicle.a = 1.3; % length from front axle to CG (m)
vehicle.L = 2.6; % wheelbase (m)
vehicle.b = 1.3; % length from rear axle to CG (m)
vehicle.d = 1.5; % track width (m)
vehicle.h_cg = 0.42; % height of the cg (m)
vehicle.Ca = [95000; 110000]; % wheel cornering stiffnesses
vehicle.Cx = [65000; 65000]; % longitudinal stiffnesses
%% Define inputs to the vehicle model
U = 24.59; % longitudinal velocity [m/s]
V = 0.0; % lateral velocity [m/s]
r = 0.5; % yaw rate [rad/s]
steering_amplitude = 2*pi/180; % front steering angle [rad]
Period = 3; % Units are seconds. A typical lane change is about 3 to 4 seconds based on experimental highway measurements
% Define items used to determine how long to run sim
TotalTime = 5; % This is how long the simulation will run.
deltaT = 0.01;
N_timeSteps = floor(TotalTime/deltaT)+1; % This is the number of time steps we should have
%% Main code
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%% Run the simulation in MATLAB
% variables to store outputs of Matlab simulation
matlab_alpha = nan(N_timeSteps,2);
matlab_time = nan(N_timeSteps,1);
counter = 1;
for t = 0:deltaT:TotalTime
matlab_time(counter) = t;
%% Inputs
delta_f = (1-1*(0<t-Period))*steering_amplitude*sin((2*pi/Period)*t); % front steering angle
steering_angle = [delta_f; 0];
Vx = abs(U*sin((0.5*pi/Period)*t + pi/2));
Vy = V*sin((pi/Period)*t);
yaw_rate = r*sin((2*pi/Period)*t);
%% Slips
% Slip Angle/Lateral Slip
slip_angle = fcn_VD_stSlipAngle(Vx,Vy,yaw_rate,steering_angle,vehicle);
matlab_alpha(counter,:) = slip_angle';
counter = counter+1;
end
%% Plot results
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% _____ _ _ _ _
% | __ \| | | | | | (_)
% | |__) | | ___ | |_| |_ _ _ __ __ _
% | ___/| |/ _ \| __| __| | '_ \ / _` |
% | | | | (_) | |_| |_| | | | | (_| |
% |_| |_|\___/ \__|\__|_|_| |_|\__, |
% __/ |
% |___/
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
fcn_VD_plotTimeSlipAngle(matlab_time,matlab_alpha);

## Slide 6: Wheel slips at each tire of a vehicle represented by the bicycle model are given by
where
function wheel_slip = fcn_VD_stWheelSlip(U,V,r,wheel_angular_velocity,...
steering_angle,vehicle)
%% fcn_VD_stWheelSlip
% This function computes Wheel Slip/Longitudinal Slip for front and rear wheels.
% It uses single-track/bicycle vehicle model.
%
%% Calculate Longitudinal Slip
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
wheel_slip = nan(2,1); % Initialize a variable
wheel_velocity = fcn_VD_stWheelVelocity(U,V,r,vehicle); % calculate wheel velocities
wheel_longitudinal_velocity = wheel_velocity(:,1).*cos(steering_angle)+...
wheel_velocity(:,2).*sin(steering_angle); % velocity of wheel along the wheel direction
wheel_longitudinal_velocity(0==wheel_longitudinal_velocity) = eps;
% Wheel-Slip calculation
wheel_slip(0>wheel_longitudinal_velocity) = 0;
% wheel slip is calculated only when the tire is moving in the direction it
% is pointed
target_indices = 0<=wheel_longitudinal_velocity;
wheel_slip(target_indices) = (vehicle.Re.*wheel_angular_velocity(target_indices)-...
wheel_longitudinal_velocity(target_indices))./...
wheel_longitudinal_velocity(target_indices);
% Saturation
wheel_slip(1<wheel_slip) = 1; % maximum wheel slip
wheel_slip(-1>wheel_slip) = -1; % minimum wheel slip
end

## Slide 7: `fcn_VD_stWheelSlip’ estimates wheel slip
%% script_testfcn_VD_stWheelSlip.m
% This script tests MATLAB function 'fcn_VD_stWheelSlip'
%
% Author: Satya Prasad on 2021/08/13
% Questions or comments? szm888@psu.edu
%% Prepare the workspace
close all; % close all the plots
clear all %#ok<CLALL>
clc
%% Add path
addpath('../VD_Utilities')
addpath('../VD_Utilities/Bicycle')
%% Inputs
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% _____ _
% |_ _| | |
% | | _ __ _ __ _ _| |_ ___
% | | | '_ \| '_ \| | | | __/ __|
% _| |_| | | | |_) | |_| | |_\__ \
% |_____|_| |_| .__/ \__,_|\__|___/
% | |
% |_|
% See: http://patorjk.com/software/taag/#p=display&f=Big&t=Inputs
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%% Define vehicle properties
% Define a MATLAB structure that specifies the physical values for a vehicle.
% For convenience, we ask that you call this stucture 'vehicle'.
vehicle.m = 1600; % mass (kg)
vehicle.Izz = 2500; % mass moment of inertia (kg m^2)
vehicle.Iw = 1.2; % mass moment of inertia of a wheel (kg m^2)
vehicle.Re = 0.32; % effective radius of a wheel (m)
vehicle.a = 1.3; % length from front axle to CG (m)
vehicle.L = 2.6; % wheelbase (m)
vehicle.b = 1.3; % length from rear axle to CG (m)
vehicle.d = 1.5; % track width (m)
vehicle.h_cg = 0.42; % height of the cg (m)
vehicle.Ca = [95000; 110000]; % wheel cornering stiffnesses
vehicle.Cx = [65000; 65000]; % longitudinal stiffnesses
%% Define inputs to the vehicle model
U = 24.59; % longitudinal velocity [m/s]
V = 0.0; % lateral velocity [m/s]
r = 0.5; % yaw rate [rad/s]
omega = 0.98*U/vehicle.Re*ones(2,1); % angular velocity of wheel [rad/s]
steering_amplitude = 2*pi/180; % front steering angle [rad]
Period = 3; % Units are seconds. A typical lane change is about 3 to 4 seconds based on experimental highway measurements
% Define items used to determine how long to run sim
TotalTime = 5; % This is how long the simulation will run.
deltaT = 0.01;
N_timeSteps = floor(TotalTime/deltaT)+1; % This is the number of time steps we should have
%% Main code
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%% Run the simulation in MATLAB
% variables to store outputs of Matlab simulation
matlab_kappa = nan(N_timeSteps,2);
matlab_time = nan(N_timeSteps,1);
counter = 1;
for t = 0:deltaT:TotalTime
matlab_time(counter) = t;
%% Inputs
delta_f = (1-1*(0<t-Period))*steering_amplitude*sin((2*pi/Period)*t); % front steering angle
steering_angle = [delta_f; 0];
Vx = abs(U*sin((0.5*pi/Period)*t + pi/2));
Vy = V*sin((pi/Period)*t);
yaw_rate = r*sin((2*pi/Period)*t);
%% Slips
% Wheel Slip/Longitudinal Slip
wheel_slip = fcn_VD_stWheelSlip(Vx,Vy,yaw_rate,omega,steering_angle,vehicle);
matlab_kappa(counter,:) = wheel_slip';
counter = counter+1;
end
%% Plot results
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% _____ _ _ _ _
% | __ \| | | | | | (_)
% | |__) | | ___ | |_| |_ _ _ __ __ _
% | ___/| |/ _ \| __| __| | '_ \ / _` |
% | | | | (_) | |_| |_| | | | | (_| |
% |_| |_|\___/ \__|\__|_|_| |_|\__, |
% __/ |
% |___/
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
fcn_VD_plotTimeWheelSlip(matlab_time,matlab_kappa);

## Slide 8: Normal forces at each tire of a vehicle represented by the bicycle model are given by
function normal_force = fcn_VD_stNormalForce(acceleration,vehicle,...
road_properties,type_of_transfer)
%% fcn_VD_stNormalForce
% This function calculates normal force on both wheels.
% It uses single-track/bicycle vehicle model.
%
%% Calculate Normal Forces
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
g = 9.81; % [m/s^2]
Fz_front = vehicle.m*g*cos(road_properties.bank_angle)*cos(road_properties.grade)*...
(vehicle.b-vehicle.h_cg*tan(road_properties.grade))/vehicle.L;
Fz_rear = vehicle.m*g*cos(road_properties.bank_angle)*cos(road_properties.grade)*...
(vehicle.a+vehicle.h_cg*tan(road_properties.grade))/vehicle.L;
normal_force = [Fz_front; Fz_rear]; % load transfer due to grade and bank
if strcmpi(type_of_transfer,'longitudinal') % Only Longitudinal Transfer
Fz_longitudinal = vehicle.m*acceleration(1)*(vehicle.h_cg/vehicle.L)*[-1; 1];
normal_force = normal_force + Fz_longitudinal;
end
end

## Slide 9: `fcn_VD_stNormalForce’ estimates normal force
%% script_test_fcn_VD_stNormalForce.m
% This script tests MATLAB function 'fcn_VD_stNormalForce'
%
% Author: Satya Prasad on 2021/08/13
% Questions or comments? szm888@psu.edu
%% Prepare the workspace
close all; % close all the plots
clear all %#ok<CLALL>
clc
%% Add path
addpath('../VD_Utilities')
addpath('../VD_Utilities/Bicycle')
%% Inputs
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% _____ _
% |_ _| | |
% | | _ __ _ __ _ _| |_ ___
% | | | '_ \| '_ \| | | | __/ __|
% _| |_| | | | |_) | |_| | |_\__ \
% |_____|_| |_| .__/ \__,_|\__|___/
% | |
% |_|
% See: http://patorjk.com/software/taag/#p=display&f=Big&t=Inputs
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%% Define vehicle properties
% Define a MATLAB structure that specifies the physical values for a vehicle.
% For convenience, we ask that you call this stucture 'vehicle'.
vehicle.m = 1600; % mass (kg)
vehicle.Izz = 2500; % mass moment of inertia (kg m^2)
vehicle.Iw = 1.2; % mass moment of inertia of a wheel (kg m^2)
vehicle.Re = 0.32; % effective radius of a wheel (m)
vehicle.a = 1.3; % length from front axle to CG (m)
vehicle.L = 2.6; % wheelbase (m)
vehicle.b = 1.3; % length from rear axle to CG (m)
vehicle.d = 1.5; % track width (m)
vehicle.h_cg = 0.42; % height of the cg (m)
vehicle.Ca = [95000; 110000]; % wheel cornering stiffnesses
vehicle.Cx = [65000; 65000]; % longitudinal stiffnesses
%% Define load transfer conditions
type_of_transfer = 'longitudinal';
% type_of_transfer = 'default';
%% Define inputs to the vehicle model
road_properties.grade = 0; road_properties.bank_angle = 0; % road properties
acceleration = [2, 0.5]; % acceleration
Period = 3; % Units are seconds. A typical lane change is about 3 to 4 seconds based on experimental highway measurements
% Define items used to determine how long to run sim
TotalTime = 5; % This is how long the simulation will run.
deltaT = 0.01;
N_timeSteps = floor(TotalTime/deltaT)+1; % This is the number of time steps we should have
%% Main code
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%% Run the simulation in MATLAB
% variables to store outputs of Matlab simulation
matlab_Fz = nan(N_timeSteps,2);
matlab_time = nan(N_timeSteps,1);
counter = 1;
for t = 0:deltaT:TotalTime
matlab_time(counter) = t;
%% Inputs
ax = acceleration(1)*sin(pi/Period*t);
ay = acceleration(2)*sin(pi/Period*t);
%% Normal Forces
normal_force = fcn_VD_stNormalForce([ax;ay],vehicle,road_properties,...
type_of_transfer);
matlab_Fz(counter,:) = normal_force';
counter = counter+1;
end
%% Plot results
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% _____ _ _ _ _
% | __ \| | | | | | (_)
% | |__) | | ___ | |_| |_ _ _ __ __ _
% | ___/| |/ _ \| __| __| | '_ \ / _` |
% | | | | (_) | |_| |_| | | | | (_| |
% |_| |_|\___/ \__|\__|_|_| |_|\__, |
% __/ |
% |___/
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
fcn_VD_plotTimeNormalForce(matlab_time,matlab_Fz);

## Slide 10: Tire forces at each tire of a vehicle given by the brush model are
function tire_force = fcn_VD_stTireForceBrush(slip_angle,wheel_slip,...
normal_force,friction_coefficient,vehicle)
%% fcn_VD_stTireForceBrush
% This function computes tire forces using Combined-Slip Brush Model.
% Ref: Tire Modeling and Friction Estimation by Jacob Svendenius
% It uses single-track/bicycle vehicle model and brush tire model.
%
%% Calculate Tire Forces using Brush Model
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
combined_slip = fcn_VD_stCombinedSlip(slip_angle,wheel_slip); % calculate combined slip
sigma_x = combined_slip(:,1);
sigma_y = combined_slip(:,2);
sigma = sqrt(sigma_x.^2 + sigma_y.^2);
sigma(0==sigma) = eps; % To avoid division by zero
% eq 4.10, 4.13 on pg 44
Psi = sqrt((vehicle.Cx.*sigma_x).^2 + (vehicle.Ca.*sigma_y).^2)./...
abs(3*friction_coefficient.*normal_force); % use peak-friction here
Psi(1<=Psi) = 1; % account for pure slip
% Adhesion forces:
% eq 4.14 on pg 44
Fax = vehicle.Cx.*sigma_x.*((1-Psi).^2);
Fay = -vehicle.Ca.*sigma_y.*((1-Psi).^2);
% Slide forces:
% eq 4.17 on pg 46
Fsz = normal_force.*(Psi.^2).*(3-2*Psi);
% eq 4.18 on pg 46
Fsx = (sigma_x./sigma).*friction_coefficient.*Fsz; % use sliding-friction here
Fsy = -(sigma_y./sigma).*friction_coefficient.*Fsz; % use sliding-friction here
tire_force = [Fax+Fsx, Fay+Fsy];
end

## Slide 11: `fcn_VD_stTireForceBrush’ estimates tire forces
%% script_test_fcn_VD_stTireForceBrush.m
% This script tests MATLAB function 'fcn_VD_stTireForceBrush'
%
% Author: Satya Prasad on 2021/08/13
% Questions or comments? szm888@psu.edu
%% Prepare the workspace
close all; % close all the plots
clear all %#ok<CLALL>
clc
%% Add path
addpath('../VD_Utilities')
addpath('../VD_Utilities/Bicycle')
%% Inputs
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% _____ _
% |_ _| | |
% | | _ __ _ __ _ _| |_ ___
% | | | '_ \| '_ \| | | | __/ __|
% _| |_| | | | |_) | |_| | |_\__ \
% |_____|_| |_| .__/ \__,_|\__|___/
% | |
% |_|
% See: http://patorjk.com/software/taag/#p=display&f=Big&t=Inputs
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%% Define vehicle properties
% Define a MATLAB structure that specifies the physical values for a vehicle.
% For convenience, we ask that you call this stucture 'vehicle'.
vehicle.m = 1600; % mass (kg)
vehicle.Izz = 2500; % mass moment of inertia (kg m^2)
vehicle.Iw = 1.2; % mass moment of inertia of a wheel (kg m^2)
vehicle.Re = 0.32; % effective radius of a wheel (m)
vehicle.a = 1.3; % length from front axle to CG (m)
vehicle.L = 2.6; % wheelbase (m)
vehicle.b = 1.3; % length from rear axle to CG (m)
vehicle.d = 1.5; % track width (m)
vehicle.h_cg = 0.42; % height of the cg (m)
vehicle.Ca = [95000; 110000]; % wheel cornering stiffnesses
vehicle.Cx = [65000; 65000]; % longitudinal stiffnesses
%% Define load transfer conditions
type_of_transfer = 'longitudinal';
% type_of_transfer = 'default';
%% Define inputs to the vehicle model
U = 24.59; % longitudinal velocity [m/s]
V = 0; % lateral velocity [m/s]
r = 0.5; % yaw rate [rad/s]
omega = 0.98*U/vehicle.Re*ones(2,1); % angular velocity of wheel [rad/s]
steering_amplitude = 2*pi/180; % front steering angle [rad]
road_properties.grade = 0; road_properties.bank_angle = 0; % road properties
acceleration = [2, 0.5]; % acceleration
friction_coefficient = [0.9; 0.9];
Period = 3; % Units are seconds. A typical lane change is about 3 to 4 seconds based on experimental highway measurements
% Define items used to determine how long to run sim
TotalTime = 5; % This is how long the simulation will run.
deltaT = 0.01;
N_timeSteps = floor(TotalTime/deltaT)+1; % This is the number of time steps we should have
%% Main code
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%% Run the simulation in MATLAB
% variables to store outputs of Matlab simulation
matlab_Fx = nan(N_timeSteps,2); matlab_Fy = nan(N_timeSteps,2);
matlab_time = nan(N_timeSteps,1);
counter = 1;
for t = 0:deltaT:TotalTime
matlab_time(counter) = t;
%% Inputs
delta_f = (1-1*(0<t-Period))*steering_amplitude*sin((2*pi/Period)*t); % front steering angle
steering_angle = [delta_f; 0];
Vx = abs(U*sin((0.5*pi/Period)*t + pi/2));
Vy = V*sin((pi/Period)*t);
yaw_rate = r*sin((2*pi/Period)*t);
ax = acceleration(1)*sin(pi/Period*t);
ay = acceleration(2)*sin(pi/Period*t);
%% Slips
% Slip Angle/Lateral Slip
slip_angle = fcn_VD_stSlipAngle(Vx,Vy,yaw_rate,steering_angle,vehicle);
% Wheel Slip/Longitudinal Slip
wheel_slip = fcn_VD_stWheelSlip(Vx,Vy,yaw_rate,omega,steering_angle,vehicle);
%% Normal Forces
normal_force = fcn_VD_stNormalForce([ax;ay],vehicle,road_properties,...
type_of_transfer);
%% Tire Forces
tire_force = fcn_VD_stTireForceBrush(slip_angle,wheel_slip,normal_force,...
friction_coefficient,vehicle);
matlab_Fx(counter,:) = tire_force(:,1)';
matlab_Fy(counter,:) = tire_force(:,2)';
counter = counter+1;
end
%% Plot results
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% _____ _ _ _ _
% | __ \| | | | | | (_)
% | |__) | | ___ | |_| |_ _ _ __ __ _
% | ___/| |/ _ \| __| __| | '_ \ / _` |
% | | | | (_) | |_| |_| | | | | (_| |
% |_| |_|\___/ \__|\__|_|_| |_|\__, |
% __/ |
% |___/
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
fcn_VD_plotTimeLongitudinalTireForce(matlab_time,matlab_Fx);
fcn_VD_plotTimeLateralTireForce(matlab_time,matlab_Fy);

## Slide 12: Body forces are derived from tire forces as below.
function body_variable = fcn_VD_stWheel2BodyCoordinates(wheel_variable,...
steering_angle)
%% fcn_VD_stWheel2BodyCoordinates
% This function transforms variables from wheel to body coordinates
% It uses single-track\bicycle vehicle model.
%
%% Convert from Wheel to Body Coordinates
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
body_variable = nan(2,2);
body_variable(:,1) = wheel_variable(:,1).*cos(steering_angle)-...
wheel_variable(:,2).*sin(steering_angle);
body_variable(:,2) = wheel_variable(:,1).*sin(steering_angle)+...
wheel_variable(:,2).*cos(steering_angle);
end

## Slide 13: State equations of the vehicle represented by bicycle model are
function acceleration = fcn_VD_st5dofForceEquation(wheel_force,wheel_torque,...
steering_angle,vehicle,road_properties)
%% fcn_VD_st5dofForceEquation
% This function calculates accelerations.
%
%% Calculate accelerations
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
g = 9.81; % [m/s^2]
body_force = fcn_VD_stWheel2BodyCoordinates(wheel_force,steering_angle); % find body forces
% Force and torque balance on the vehicle body
ax = sum(body_force(:,1))/vehicle.m-g*cos(road_properties.bank_angle)*sin(road_properties.grade); % longitudinal acceleration
ay = sum(body_force(:,2))/vehicle.m+g*sin(road_properties.bank_angle); % lateral acceleration
drdt = ((vehicle.a*body_force(1,2))-(vehicle.b*body_force(2,2)))/vehicle.Izz; % yaw acceleration
% Torque balance on vehicle's wheels
domegadt = (wheel_torque-vehicle.Re.*wheel_force(:,1))./vehicle.Iw; % angular acceleration of wheel
acceleration = [ax; ay; drdt; domegadt];
end

## Slide 14: Vehicle motion is represented in global coordinates is related to the motion in local coordinates as
function dydt = fcn_VD_Body2GlobalCoordinates(~, y, U, V, r)
%% fcn_VD_Body2GlobalCoordinates
% This function calculates velocites in global coordinates.
%
%% Calculate velocities in Global coordinates
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
psi = y(3);
dXdt = U*cos(psi)-V*sin(psi);
dYdt = U*sin(psi)+V*cos(psi);
dPhidt = r;
dydt = [dXdt; dYdt; dPhidt];
end

## Slide 15: MATLAB implementation of the 5-dof vehicle model is
function dydt = fcn_VD_st5dofModel(t,y,...
steering_amplitude,Period,wheel_torque,...
vehicle,road_properties,friction_coefficient,type_of_transfer)
%% fcn_VD_st5dofModel
% This function sets-up a 5-DoF Single-Track vehicle model using Brush
% tire model. This works without controller but with time dependent inputs.
%
global flag_update global_acceleration % change the variable name based on the matlab script
persistent delayed_acceleration % variable to store acceleration in the previous time-step
%% Implement 5-DoF Vehicle Model
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
U = y(1); % longitudinal velocity [m/s]
V = y(2); % lateral velocity [m/s]
r = y(3); % yaw rate [rad/s]
omega = y(4:5); % angular velocity of wheels [rad/s]
pose = y(6:8); % position and orientation of the vehicle
%% Steering Input
delta_f = (1-1*(0<t-Period))*steering_amplitude*sin((2*pi/Period)*t); % front steering angle [rad]
steering_angle = [delta_f; 0];
%% Slips
% Slip Angle/Lateral Slip
slip_angle = fcn_VD_stSlipAngle(U,V,r,steering_angle,vehicle);
% Wheel Slip/Longitudinal Slip
wheel_slip = fcn_VD_stWheelSlip(U,V,r,omega,steering_angle,vehicle);
%% Normal Forces
if flag_update
% load transfer is calculated based on the acceleration in the previous
% time-step 't-deltaT'
delayed_acceleration = global_acceleration;
end
normal_force = fcn_VD_stNormalForce(delayed_acceleration(1:2),vehicle,...
road_properties,type_of_transfer);
%% Tire Forces
tire_force = fcn_VD_stTireForceBrush(slip_angle,wheel_slip,normal_force,...
friction_coefficient,vehicle);
%% Newtonian Dynamics
acceleration = fcn_VD_st5dofForceEquation(tire_force,wheel_torque,...
steering_angle,vehicle,road_properties);
DvelDt = fcn_VD_5dofStateEquation(t,y(1:5),acceleration);
if flag_update
% 'global_acceleration' will be updated only in the first call to the
% function in RK4 method i.e., while computing k1 in 'fcn_VD_RungeKutta'
global_acceleration = acceleration;
flag_update = false;
end
%% Body2Global coordinates
DposeDt = fcn_VD_Body2GlobalCoordinates(t,pose,U,V,r);
%% Write to output
dydt = [DvelDt; DposeDt];
end

## Slide 16: Simulink implementation of the 5-dof vehicle model is
function dydt = fcn_VD_st5dofModel(t,y,...
steering_amplitude,Period,wheel_torque,...
vehicle,road_properties,friction_coefficient,type_of_transfer)
%% fcn_VD_st5dofModel
% This function sets-up a 5-DoF Single-Track vehicle model using Brush
% tire model. This works without controller but with time dependent inputs.
%
global flag_update global_acceleration % change the variable name based on the matlab script
persistent delayed_acceleration % variable to store acceleration in the previous time-step
%% Implement 5-DoF Vehicle Model
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
U = y(1); % longitudinal velocity [m/s]
V = y(2); % lateral velocity [m/s]
r = y(3); % yaw rate [rad/s]
omega = y(4:5); % angular velocity of wheels [rad/s]
pose = y(6:8); % position and orientation of the vehicle
%% Steering Input
delta_f = (1-1*(0<t-Period))*steering_amplitude*sin((2*pi/Period)*t); % front steering angle [rad]
steering_angle = [delta_f; 0];
%% Slips
% Slip Angle/Lateral Slip
slip_angle = fcn_VD_stSlipAngle(U,V,r,steering_angle,vehicle);
% Wheel Slip/Longitudinal Slip
wheel_slip = fcn_VD_stWheelSlip(U,V,r,omega,steering_angle,vehicle);
%% Normal Forces
if flag_update
% load transfer is calculated based on the acceleration in the previous
% time-step 't-deltaT'
delayed_acceleration = global_acceleration;
end
normal_force = fcn_VD_stNormalForce(delayed_acceleration(1:2),vehicle,...
road_properties,type_of_transfer);
%% Tire Forces
tire_force = fcn_VD_stTireForceBrush(slip_angle,wheel_slip,normal_force,...
friction_coefficient,vehicle);
%% Newtonian Dynamics
acceleration = fcn_VD_st5dofForceEquation(tire_force,wheel_torque,...
steering_angle,vehicle,road_properties);
DvelDt = fcn_VD_5dofStateEquation(t,y(1:5),acceleration);
if flag_update
% 'global_acceleration' will be updated only in the first call to the
% function in RK4 method i.e., while computing k1 in 'fcn_VD_RungeKutta'
global_acceleration = acceleration;
flag_update = false;
end
%% Body2Global coordinates
DposeDt = fcn_VD_Body2GlobalCoordinates(t,pose,U,V,r);
%% Write to output
dydt = [DvelDt; DposeDt];
end

## Slide 17: Dual Track Model of a vehicle represents left wheel separate from the right unlike bicycle model
CG
a
b
d

## Slide 18: Slip angles/lateral slip at each tire of a vehicle represented by the dual-track model are given by

## Slide 19: `mdl_dtSlipAngle’ is the Simulink model to estimate slip angles.

## Slide 20: `fcn_VD_dtWheelVelocity’ is the Matlab function to estimate wheel velocities.
function wheel_velocity = fcn_VD_dtWheelVelocity(U,V,r,vehicle)
%% fcn_VD_dtWheelVelocity
% This function computes velocities for front left, front right,
% rear left and rear right wheels.
% It uses double-track vehicle model.
%
%% Calculate Wheel Velocities in body coordinates
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
wheel_velocity = nan(4,2); % Initialize a variable
% Velocity of wheel along vehicle body (X-Direction)
wheel_velocity([1,3],1) = U-0.5*vehicle.d*r; % Left tires
wheel_velocity([2,4],1) = U+0.5*vehicle.d*r; % Right tires
% Velocity of wheel perpendicular to vehicle body (Y-Direction)
wheel_velocity([1,2],2) = V+vehicle.a*r; % Front tires
wheel_velocity([3,4],2) = V-vehicle.b*r; % Rear tires
end

## Slide 21: `fcn_VD_dtSlipAngle’ is the Matlab function to estimate slip angles.
function slip_angle = fcn_VD_dtSlipAngle(U,V,r,steering_angle,vehicle)
%% fcn_VD_dtSlipAngle
% This function computes Slip Angles/Lateral Slip for front left,
% front right, rear left and rear right wheels.
% It uses double-track vehicle model.
%
%% Calculate Slip-Angles
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
wheel_velocity = fcn_VD_dtWheelVelocity(U,V,r,vehicle); % calculate wheel velocities
slip_angle = atan(wheel_velocity(:,2)./wheel_velocity(:,1))-steering_angle; % calculate slip angles
end

## Slide 22: Wheel/longitudinal slips at each tire of a vehicle represented by the dual-track model are given by
where

## Slide 23: `mdl_dtWheelSlip’ is the Simulink model to estimate wheel slip.
Tire longitudinal velocity
Wheel slip

## Slide 24: `fcn_VD_dtWheelSlip’ is the Matlab function to estimate wheel slip.
function wheel_slip = fcn_VD_dtWheelSlip(U,V,r,wheel_angular_velocity,...
steering_angle,vehicle)
%% fcn_VD_longitudinalSlipDualTrack
% This function computes Wheel Slip/Longitudinal Slip for front left,
% front right, rear left and rear right wheels.
% It uses double-track vehicle model.
%
%% Calculate Longitudinal Slip
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
wheel_slip = nan(4,1); % Initialize a variable
wheel_velocity = fcn_VD_dtWheelVelocity(U,V,r,vehicle); % calculate wheel velocities
wheel_longitudinal_velocity = wheel_velocity(:,1).*cos(steering_angle)+...
wheel_velocity(:,2).*sin(steering_angle); % velocity of wheel along the wheel direction
wheel_longitudinal_velocity(0==wheel_longitudinal_velocity) = eps;
% Wheel-Slip calculation
wheel_slip(0>=wheel_longitudinal_velocity) = 0;
% wheel slip is calculated only when the tire is moving in the direction it
% is pointed
target_indices = 0<wheel_longitudinal_velocity;
wheel_slip(target_indices) = (vehicle.Re.*wheel_angular_velocity(target_indices)-...
wheel_longitudinal_velocity(target_indices))./...
wheel_longitudinal_velocity(target_indices);
% Saturation
wheel_slip(1<wheel_slip) = 1; % maximum wheel slip
wheel_slip(-1>wheel_slip) = -1; % minimum wheel slip
end

## Slide 25: Normal forces at each tire of a vehicle represented by the dual-track model are given by

## Slide 26: `mdl_dtNormalForce’ is the Simulink model to estimate normal forces.
Static load

## Slide 27: `mdl_dtNormalForce’ is the Simulink model to estimate normal forces.
Longitudinal transfer
Lateral transfer

## Slide 28: `fcn_VD_dtNormalForce’ is the Matlab function to estimate normal forces.
function normal_force = fcn_VD_dtNormalForce(acceleration,vehicle,...
road_properties,type_of_transfer)
%% fcn_VD_dtNormalForce
% This function calculates normal force on all the four wheels.
% It uses double-track vehicle model.
%
%% Calculate Normal Forces
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
g = 9.81; % [m/s^2]
Fz_front = 0.5*vehicle.m*g*cos(road_properties.bank_angle)*cos(road_properties.grade)*...
(vehicle.b-vehicle.h_cg*tan(road_properties.grade))/vehicle.L;
Fz_rear = 0.5*vehicle.m*g*cos(road_properties.bank_angle)*cos(road_properties.grade)*...
(vehicle.a+vehicle.h_cg*tan(road_properties.grade))/vehicle.L;
Fz_lateral_static = vehicle.m*g*sin(road_properties.bank_angle)*(vehicle.h_cg/vehicle.d)*...
([vehicle.b; -vehicle.b; vehicle.a; -vehicle.a]/vehicle.L);
normal_force = [Fz_front; Fz_front; Fz_rear; Fz_rear]+Fz_lateral_static; % load transfer due to grade and bank
if strcmpi(type_of_transfer,'both') % Both Longitudinal and Lateral Transfer
Fz_longitudinal = vehicle.m*acceleration(1)*(vehicle.h_cg/vehicle.L)*[-0.5; -0.5; 0.5; 0.5];
Fz_lateral = vehicle.m*acceleration(2)*(vehicle.h_cg/vehicle.d)*([-vehicle.b; vehicle.b; -vehicle.a; vehicle.a]/vehicle.L);
normal_force = normal_force + Fz_longitudinal + Fz_lateral;
elseif strcmpi(type_of_transfer,'longitudinal') % Only Longitudinal Transfer
Fz_longitudinal = vehicle.m*acceleration(1)*(vehicle.h_cg/vehicle.L)*[-0.5; -0.5; 0.5; 0.5];
normal_force = normal_force + Fz_longitudinal;
end
end

## Slide 29: Tire forces at each tire of a vehicle represented by the dual-track model are given by

## Slide 30: `mdl_dtTireForceBrush’ is the Simulink model to estimate tire forces using the brush tire model.
Combined slip

## Slide 31: `fcn_VD_dtCombinedSlip’ is the Matlab function to estimate combined slips.
function combined_slip = fcn_VD_dtCombinedSlip(slip_angle,wheel_slip)
%% fcn_VD_dtCombinedSlip
% This function computes Combined Slip for front left, front right,
% rear left and rear right wheels.
% It uses double-track vehicle model.
%
%% Calculate Combined Slip
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
combined_slip = nan(4,2); % Initialize a variable
denominator = wheel_slip+1; % denominator that's used in calculating combined slip
denominator(0==denominator) = eps; % to avoid division by zero
combined_slip(:,1) = wheel_slip./denominator; % sigma-x
combined_slip(:,2) = tan(slip_angle)./denominator; % sigma-y
end

## Slide 32: `mdl_dtTireForceBrush’ is the Simulink model to estimate tire forces using the brush tire model.
Tire forces

## Slide 33: `fcn_VD_dtTireForceBrush’ is the Matlab function to estimate tire forces using the brush tire model.
function tire_force = fcn_VD_dtTireForceBrush(slip_angle,wheel_slip,...
normal_force,friction_coefficient,vehicle)
%% fcn_VD_dtTireForceBrush
% This function computes tire forces using Combined-Slip Brush Model.
% Ref: Tire Modeling and Friction Estimation by Jacob Svendenius
% It uses double-track vehicle model and brush tire model.
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
combined_slip = fcn_VD_dtCombinedSlip(slip_angle,wheel_slip); % calculate combined slip
sigma_x = combined_slip(:,1);
sigma_y = combined_slip(:,2);
sigma = sqrt(sigma_x.^2 + sigma_y.^2);
sigma(0==sigma) = eps; % To avoid division by zero
% eq 4.10, 4.13 on pg 44
Psi = sqrt((vehicle.Cx.*sigma_x).^2 + (vehicle.Ca.*sigma_y).^2)./...
abs(3*friction_coefficient.*normal_force); % use peak-friction here
Psi(1<=Psi) = 1; % account for pure slip
% Adhesion forces:
% eq 4.14 on pg 44
Fax = vehicle.Cx.*sigma_x.*((1-Psi).^2);
Fay = -vehicle.Ca.*sigma_y.*((1-Psi).^2);
% Slide forces:
% eq 4.17 on pg 46
Fsz = normal_force.*(Psi.^2).*(3-2*Psi);
% eq 4.18 on pg 46
Fsx = (sigma_x./sigma).*friction_coefficient.*Fsz; % use sliding-friction here
Fsy = -(sigma_y./sigma).*friction_coefficient.*Fsz; % use sliding-friction here
tire_force = [Fax+Fsx, Fay+Fsy];
end

## Slide 34: Aligning moment at each tire of a vehicle represented by the dual-track model is given by

## Slide 35: `mdl_dtAligningMomentBrush’ is the Simulink model to estimate aligning moment using the brush tire model.
Aligning moment

## Slide 36: `fcn_VD_dtAligningMomentBrush’ is the Matlab function to estimate aligning moment using the brush tire model.
function aligning_moment = fcn_VD_dtAligningMomentBrush(slip_angle,...
normal_force,friction_coefficient,vehicle)
%% fcn_VD_dtAligningMomentBrush
% This function calculates aligning moment on all the four wheels.
% Reference: https://www.tandfonline.com/doi/full/10.1080/00423114.2019.1580377
% It uses double-track vehicle model and brush tire model.
%
%% Calculate Aligning Moment
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% equation 13a, 13b on pg 9
Xi1 = (vehicle.contact_patch_length*vehicle.Ca.*tan(slip_angle))/3;
Xi2 = ((2-vehicle.friction_ratio)*vehicle.contact_patch_length*(vehicle.Ca.^2).*(tan(slip_angle).^2))/3;
Xi3 = ((1-2*vehicle.friction_ratio/3)*vehicle.contact_patch_length*(vehicle.Ca.^3).*(tan(slip_angle).^3))/3;
Xi4 = ((4/27-vehicle.friction_ratio/9)*vehicle.contact_patch_length*(vehicle.Ca.^4).*(tan(slip_angle).^4))/3;
% equation 12 on pg 9
aligning_moment = Xi1-...
Xi2./(friction_coefficient.*normal_force)+...
Xi3./((friction_coefficient.*normal_force).^2)-...
Xi4./((friction_coefficient.*normal_force).^3);
% check for saturation
saturation_test = (3*friction_coefficient.*normal_force)./vehicle.Ca-abs(tan(slip_angle));
aligning_moment(0>=saturation_test) = 0;
end

## Slide 37: Tire forces along the longitudinal and lateral direction of the vehicle are given by

## Slide 38: Simulink model to estimate tire forces along the longitudinal and lateral direction.

## Slide 39: `fcn_VD_dtWheel2BodyCoordinates’ is the Matlab function to estimate tire forces along the longitudinal and lateral direction.
function body_variable = fcn_VD_dtWheel2BodyCoordinates(wheel_variable,...
steering_angle)
%% fcn_VD_dtWheel2BodyCoordinates
% This function transforms variables from wheel to body coordinates
% It uses double-track vehicle model.
%
%% Convert from Wheel to Body Coordinates
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
body_variable = nan(4,2);
body_variable(:,1) = wheel_variable(:,1).*cos(steering_angle)-...
wheel_variable(:,2).*sin(steering_angle);
body_variable(:,2) = wheel_variable(:,1).*sin(steering_angle)+...
wheel_variable(:,2).*cos(steering_angle);
end

## Slide 40: State equations of the 7DOF vehicle model are

## Slide 41: `fcn_VD_7dofForceEquation’ is the Matlab function for force equations of a 7DOF vehicle model.
function acceleration = fcn_VD_dt7dofForceEquation(wheel_force,wheel_torque,...
steering_angle,vehicle,road_properties)
%% fcn_VD_dt7dofForceEquation
% This function calculates accelerations.
%
%% Calculate accelerations
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
g = 9.81; % [m/s^2]
body_force = fcn_VD_dtWheel2BodyCoordinates(wheel_force,steering_angle); % find body forces
% Force and torque balance on the vehicle body
ax = sum(body_force(:,1))/vehicle.m-g*cos(road_properties.bank_angle)*sin(road_properties.grade); % longitudinal acceleration
ay = sum(body_force(:,2))/vehicle.m+g*sin(road_properties.bank_angle); % lateral acceleration
drdt = (((vehicle.d/2)*(-body_force(1,1)+body_force(2,1)-body_force(3,1)+body_force(4,1)))+...
(vehicle.a*sum(body_force([1,2],2)))-(vehicle.b*sum(body_force([3,4],2))))/vehicle.Izz; % yaw acceleration
% Torque balance on vehicle's wheels
domegadt = (wheel_torque-vehicle.Re.*wheel_force(:,1))./vehicle.Iw; % angular acceleration of wheel
acceleration = [ax; ay; drdt; domegadt];
end

## Slide 42: `fcn_VD_7dofStateEquation’ is the Matlab function for state equations of a 7DOF vehicle model.
function dydt = fcn_VD_7dofStateEquation(~,y,acceleration)
%% fcn_VD_7dofStateEquation
% This function is a differential equation for longitudinal velocity,
% lateral velocity, yaw rate, and angular velocities of wheels.
%
%% Differential equation for 7-DOF model
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
dUdt = acceleration(1)+y(3)*y(2); % Vxdot
dVdt = acceleration(2)-y(3)*y(1); % Vydot
drdt = acceleration(3); % yaw acceleration
domegadt = acceleration(4:7); % angular acceleration of wheel
dydt = [dUdt; dVdt; drdt; domegadt];
end

## Slide 43: Vehicle position in the global coordinates is given by

## Slide 44: Simulink model to estimate vehicle position in the global coordinates.

## Slide 45: `fcn_VD_dtBody2GlobalCoordinates’ is the Matlab function to estimate vehicle position in the global coordinates.
function dydt = fcn_VD_Body2GlobalCoordinates(~, y, U, V, r)
%% fcn_VD_Body2GlobalCoordinates
% This function calculates velocites in global coordinates.
%
%% Calculate velocities in Global coordinates
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
% __ __ _
% | \/ | (_)
% | \ / | __ _ _ _ __
% | |\/| |/ _` | | '_ \
% | | | | (_| | | | | |
% |_| |_|\__,_|_|_| |_|
%
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
psi = y(3);
dXdt = U*cos(psi)-V*sin(psi);
dYdt = U*sin(psi)+V*cos(psi);
dPhidt = r;
dydt = [dXdt; dYdt; dPhidt];
end

## Slide 46: Vehicle position in the global coordinates is given by

## Slide 47: Simulink model to estimate vehicle position in the global coordinates.

## Slide 48: `fcn_VD_dtBody2GlobalCoordinates’ is the Matlab function to estimate vehicle position in the global coordinates.

## Slide 49: Pure Pursuit driver model
Lateral Offset Error, e

## Slide 50: Macadam driver model
Optimal control,
Time delay, D
Final steering control,

## Slide 51: Single-Point Macadam driver model
G
u
f
Driver
Prediction
Driver
Prediction
Vehicle
Dynamics
Driver
Lag
Previewed
Error
Driver Gain
Compensation
Previewed
Path
Input
Previewed
Lateral
Displacement

## Slide 52: Driver’s ability to predict that component of the future response of the vehicle deriving only from the current steering control input

## Slide 53: Driver’s ability to predict that component of the future response of the vehicle deriving only from the present state of the vehicle

## Slide 54
CG
a
b
d